## Slide 1: Update on Surface Characterization in the GPM Combined Algorithm
Joe Munchak
With help from Bob Meneghini, Mircea Grecu, and Bill Olson

## Slide 2: Objectives
Basic idea is to move from using independent (TELSEM-based) emissivities and SRT-based PIA to internally-consistent emissivities and σ0.
  Use σ0 directly as observational constraint, instead of SRT or dSRT PIA
This should make better use of both GMI and DPR observations by restricting the initial ensemble to realistic combinations of emissivity and σ0.
  The computed σ0 includes surface variability and PIA variability in the ensemble.
Adding wind (ocean) and emissivity (land) to the retrieval output will also be useful for constellation database generation.

## Slide 3: Approach (Land)
  Develop GMI emissivity retrieval for non-precipitating pixels
  Generate databases of emissivity and σ0, including covariances (currently using same surface classification as GPROF)
  Modify retrieval by randomly perturbing EOFs of emissivity/σ0 during ensemble generation, adding multi-channel emissivity to the retrieval variables (x), and replacing PIA with (or use in conjunction with) σ0 in the observations (y)

## Slide 6: Vegetation Class Example
EOF1
EOF2
EOF3
EOF4

## Slide 7: Snow Class Example
EOF1
EOF2
EOF3
EOF4

## Slide 8: Algorithm mechanics – generate ensemble and covariances, then filter ensemble
Initial Ensemble
(Mean and Obs. Error)
Rain adjustment (mean and σ)
Emis adjustment (mean and σ)
+ Ensemble covariances
Mean Rain
Ku σ0 error
Mean 18H Emis
18H error
Rain-Ku
Rain-Ka
Rain-10V
Emis-10V

## Slide 9: Summary
Land retrieval currently being tested for possible inclusion in PPS Version 4 (late 2015/early 2016 release)
  Using GPROF surface classification (14 classes)
  Sigma_zero used in addition to PIA
  Emissivity retrieval part of output
  Impact on precipitation output being evaluated for one month (September 2014)
Future Steps:
  Explore alternate land classifications (joint emissivity-sigma_zero classes?)
  Evaluate ancillary data for dynamic surface classification
  The more tightly we can constrain the surface (without over-constraining it), the better the precipitation signal is represented in the sample covariances in the ensemble filter