## Slide 1: Development of a Satellite Passive Microwave Snowfall Detection Algorithm
Cezar Kongoli1, Huan Meng2, Jun Dong1, Ralph Ferraro2,
1University of Maryland/ESSIC/Cooperative Institute for Climate and Satellites
2NOAA/National Environmental Satellite, Data, and Information Service

## Slide 2: Product Overview
Probability-based Snowfall Detected (SD) area over global land;
Snowfall mask for 1DVAR-based SnowFall Rate (SFR) (Meng et al. 2016, submitted to JGR) generated from AMSU/MHS sensor pair (POES/Metop) and ATMS (S-NPP and the future JPSS satellites);
The five satellites produce up to ten snowfall rate estimates per day at mid-latitudes and more estimates at higher latitudes;
A similar SSMIS-based SD/SFR product is under development.
2
Retrieved Snowfall Rate
NEXRAD Reflectivity

## Slide 3: A Brief Historical Perspective (1)
Operational snow cover algorithms from VIS/IR and passive MW have over 40-year history.
Real progress on snowfall determinations began only with the launch of satellites carrying AMSU-A/B/MHS instruments. WHY?
  Very difficult to discriminate winter snowfall from no-snowfall clouds or snow on the ground using VIS/IR measurements;
  Passive MW measurements at 89 GHz and above are sensitive to snowfall-sized ice particles. WV channels around 180 GHz are even better since WV screens out surface effects.

## Slide 4: A Brief Historical Perspective (2)
MSPPS AMSU snowfall detection algorithm was the first operational product (Kongoli et al., 2003; Ferraro et al. 2005). Historical MSPPS images available at: http://www.star.nesdis.noaa.gov/corp/scsb/mspps/
A decision tree binary classification with retrievals limited to warmer weather. Colder weather retrievals were found too noisy and removed from the product.

## Slide 5: New Snowfall Detection Algorithm
Coupled principal components and logistic regression model (Kongoli et al., 2015);
Input data: 53.6 GHz and all high frequency channels above 89 (MHS) /88.2 GHz (ATMS);
Model output is the probability of snowfall; preset thresholds for snowfall;
Training data sets are composed of matching satellite and ground snowfall observation data;
Additional filters and screenings to improve the accuracy of snowfall detection.
Snowfall Freq. vs. 2 m RH

## Slide 6: Extension to Cold Regime
Satellite measurements exhibit different characteristics depending on atmospheric conditions:
  Scattering signal dominates in relatively warm and moist atmosphere
  Emission signal dominates in cold and dry atmosphere (or with abundant supercooled liquid water)
Limb-corrected temperature sounding channel 53.6 GHz (Tb53L) as a proxy for atmospheric temperature
Tb53L is used to define retrieval regimes:
Too warm, no snow (> 252K)
Warm regime (244K ~ 252K)
Cold regime (240K ~ 244K)
Too cold, no retrieval (< 240K)
SD models are trained separately for cold and warm regimes.
Snowfall Freq. vs. Tb53L

## Slide 7: Tb53L a strong predictor of near surface temperature
Snowfall
No-Snowfall

## Slide 8: Two-Regime Hypothesis
Strong Empirical Evidence: Change of direction in
the correlation between measured SFR and TBs
Variable | SFR (mm/hr) |  |  | 
 | Regime 1 Regime 2 |  |  | 
temp | 0.13 | 0.10 |  | 
hum | 0.06 | 0.10 |  | 
TB89 | -0.07 | 0.09 |  | 
TB165 | -0.20 | 0.08 |  | 
TB176 | -0.23 | 0.06 |  | 
TB179 | -0.23 | 0.04 |  | 
TB180 | -0.21 | 0.03 |  | 
TB181 | -0.17 | 0.03 |  | 
TB182 | -0.05 | -0.01 |  | 
TB53L | 0.10 | 0.10 |  | 

## Slide 9
Radar Reflectivity
Extension to Cold Regime
Cold regime extension is a new development for ATMS SFR, also applied to the AMSU/MHS algorithm
No Cold Extension
With Cold Extension

## Slide 10: New Snowfall Detection Procedure
SD Procedure
  Apply filters and determine snowfall regime;
  Run the statistical model to derive snowfall probability;
  Compare with probability threshold to obtain Snowfall Detection Index
  Apply NWP based screening to derive the final SD ‘product’.
Snowfall Probability
Snowfall Detection Index
Snowfall Rate
NEXRAD Composite Reflectivity

## Slide 11: SD Validation (1)
SD algorithm was evaluated with in-situ data as ground truth for snowfall events over CONUS and Alaska that spread out over different regions and time of year;
62% of ground truth data is very light snowfall reported as “trace” – challenging to detect for satellite product;
Evaluation included an investigation of error sources and sensitivity to the probability of snowfall, snowfall intensity, elevation, zenith angle and additional model-based screening.
Statistics:
Probability of Detection (%) | False Alarm Rate (%) | Heidke Skill Score
51 | 9.5 | 0.45

## Slide 12
SD Validation (2)
Other Conclusions
  SD performance is comparable over high and low elevation areas;
  Statistics improve with snowfall rate;
  Statistics degrade for shallow to moderate cloud snowfall;
  The most effective screening parameters are cloud thickness and relative humidity;

## Slide 13
On-going/Future Work
Hybrid weather forecast-satellite snowfall detection model
  Probability Logistic Regression model based on Numerical Weather Prediction (NWP) model data;
  Coupled Principal Components and Probability Logistic Regression model based on satellite TBs;
  Hybrid model: Optimal weighting of both:
  Prob_hybrid = W1*Prob_wea +W2*Prob_sat
  W1+W2 = 1

## Slide 14
GFS-derived weather variables considered: cloud thickness, relative humidity and vertical velocity at 1,2 and 3 km height, cloud top height and temperature;
1-km relative humidity and cloud thickness the most statistically significant to discriminate snowfall from no-snowfall cases including moderate to shallow-cloud snowfall (cloud thickness less than 3.5 km).
Weather-based Model Statistics

## Slide 15
Weather-based model Statistics (2)
Forecast relative humidity histograms at 1 km height for no-snowfall (left) and snowfall (right) cases. For rel. humidity at and above 90 %, 75% of all snowfall cases are detected with 25% false alarm.
No-snowfall
Snowfall

## Slide 16
Weather-based Model Statistics (3)
GFS-derived cloud thickness for no-snowfall (left) and snowfall (right) cases. For cloud height over 3500 m, 55% of all snowfall cases are detected with less than 10% false alarm
No-snowfall
Snowfall

## Slide 17
Weather-based Model Statistics (4)
Variables in the Equation |  |  |  |  |  |  | 
 |  | B | S.E. | Wald | df | Sig. | Exp(B)
Step 6a | Hum1 | .033 | .001 | 1440.086 | 1 | .000 | 1.033
 | Hum3 | -.004 | .001 | 29.394 | 1 | .000 | .996
 | hum | .034 | .001 | 606.497 | 1 | .000 | 1.035
 | V2 | .000 | .000 | 88.362 | 1 | .000 | 1.000
 | V3 | -.001 | .000 | 214.769 | 1 | .000 | .999
 | Cthick | .001 | .000 | 1182.353 | 1 | .000 | 1.001
 | Constant | -6.908 | .131 | 2761.055 | 1 | .000 | .001
Classification Tablea |  |  |  |  | 
 | Observed |  | Predicted |  | 
 |  |  | Snowcode |  | Percentage Correct
 |  |  | 0 | 1 | 
Step 6 | Snowcode | 0 | 22535 | 4546 | 83.2
 |  | 1 | 4644 | 11777 | 71.7
 | Overall Percentage |  |  |  | 78.9
a. The cut value is .500 |  |  |  |  | 

## Slide 18: Hybrid Model Application Examples
The blended (0.5:0.5) weather-satellite snowfall detection model for both shallow and thick-cloud snowfall
Radar Reflectivity
Deep-Cloud
Snowfall Case
Shallow-Cloud
Snowfall Case
Deep-Cloud
Snowfall Case

## Slide 19: Future Development
Development of SSMIS and GMI algorithms
Development of ocean algorithms

## Slide 20: Acknowledgement
JPSS Proving Ground and Risk Reduction Program
NOAA/NESDIS
NASA
Thank You!